## Slide 1: Telemetry

## Slide 2: Revision
Read the LT Telemetry presentation first, it contains useful background info and various tables and diagrams which I may not reproduce here.

## Slide 3: Paradigms
There are basically 2 paradigms used to obtain telemetry:-
  Polling
    Client sends a request for some sort of data.
    Server handles request, obtains data, sends back.
      Client is responsible for determining frequency of requests.
        Can miss rapid changes.
        Can overload system if polling too often.
  Pub-sub
    Client registers for specific feed(s).
    Provider sends data back as soon as available.
        Data is always most recent and fresh however fast it is changing.
        Provider may loose client registration – client does not know.

## Slide 4: Feed types
There are basically 2 types of feed available.
  Regular/continuous feeds.
    These consist typically of measured values or states which can be sampled at intervals and for which it is not necessary to have every data point.
      Mechanism positions, system states etc.
  Event-driven feeds.
    These feeds consist of events or state-changes for which the full history is needed to make sense of the data i.e. they cannot just be sampled at intervals.
      Detection of the start and end of a task or scheduling sweep.
      Seeing updates which occur at irregular intervals.

## Slide 5: Systems in use
There are 2 different telemetry systems in use at this time.
Old system – based on polling was historically used by the RCSGui.
  Due to network features, a modified version of this system is still required to obtain data for the Live Status web pages.
  It is limited to providing telemetry from the RCS on a single port.
  It is also limited to providing regularly changing feeds rather than event-driven feeds.
New system is based on pub-sub.
  Feeds are available from a number of originating systems:-
    RCS, Scheduler, EMS, TCM, ICM.
  Event-driven feeds are available.

## Slide 6: Old system
The RCS provides a JMS based control-server on port 9110.
When a GET_STATUS request is received, the server creates a handler and processes the request.
The category parameter is extracted and used to obtain a reference to a StatusProvider (for that category) from the registry.
  E.g. MECH, AUTOGUIDER, METEO, RATCAM
The individual providers having been previously registered against their category names.
The StatusCategory object is packed into a GET_STATUS_DONE and sent back to the client.
The client is responsible for deciding the polling rate.
Providers obtain their statuses in various ways:-
  Various TcsStatusClients for each TCS category.
  InstrumentStatusClients for each instrument.
  Certain internal providers within the RCS.
  E.g. SM (state model), SEEING (predecessor to SkyModel)
Most of these providers are now defunct due to the way in which status information is collated within the RCS now using TCM, ICM, EMS.

## Slide 7: Architecture – Old system

## Slide 8: Old Providers
Mostly in ngat.rcs.scm.collation package.
Implement StatusMonitorClient interface.
StatusMonitorThread associated with each
  Calls on client to obtain status from its source at configured intervals.
  TcsStatusClient (per TCS SHOW category).
  InstrumentStatusClient.
  RCSInternalStatusClient (statemodel etc).
  URLStatusClient – reading from data files e.g. cloud, dust, robodimm created by cron scripts.
Now ALL defunct.

## Slide 9: Old Telemetry Network
Old system uses a number of different mechanisms due to network restrictions.
Server push from RCS to RcsGUI and TEA – a form of simple pub-sub.
Client pull – various polled feeds from RCS to RcsGUI.
UDP from LiveStatus requestor to LiveStatus receiver.
A few pub-sub streams using new architecture.

## Slide 10: Old Network - Architecture

## Slide 11: New System
The RCS subsystems – TCM, ICM, EMS, ERS, TMS, etc and other systems e.g. SCHED, implement specific providers for the various types of status feed.
These providers act as the publishers which external clients attach to as subscribers.
Internally a provider is part of the running system, i.e. there could be a line of code at the start of some important operation (X) where a call is made to a method which sends out an event notification to subscribers.
  startingOperationX(subs); // notify registered subscribers…
It is unwise to have it make the publishing calls out to the clients directly, a slow receiver could potentially block a time-critical operation.
A gateway is introduced to handle the direct publishing from the provider.
  Gateway acts as publisher to client
  Acts as client to real provider.
  Disconnects publisher from actual client.

## Slide 12: Architecture – New system

## Slide 13: Components
Typical components which go to make up a telemetry feed/stream.
XProvider – publisher interface
  Typically has methods to add and remove subscribers
    addXListener(xl), removeXListener(xl)
XSource – an implementation of XProvider
  This is probably a class which is an integral part of the running subsystem.
XListener – listener inteface
  Typically has callback methods like
    xUpdated(Xstatus), xEventA(), xEventB(), etc
XReceiver – an implementation of XListener
  Could be a GUI component or logging class.
XArchive – archive retrieval interface
  Typically has methods to obtain historic status.
XArchiveGateway – a class which implements all the interfaces and acts as both a publisher endpoint for remote clients to connect with and keeps the key activity of the source separate from its publishing commitments to avoid blocking.

## Slide 14: Example
Telescope system telemetry feed.
BasicTelescope is the primary publisher and implements TelescopeStatusProvider.
It is also the class which collates status from the TCS and Autoguider.
TelescopeArchiveGateway subscribes to Telescope as a listener. It stores the received statuses and then posts these out to real clients under control of a processing thread.

## Slide 15: New Telemetry System
Ideally all network telemetry should be via the new pub-sub system.
RCS, Sched, TEA, NSO all feeding to clients such as OpsUI and LiveStatus.
Live Status is still however restricted to the old system but the source providers are now linked to the normal pub-sub feeds within RCS rather than collecting their own status info.
E.g. Legacy Instrument providers are fed by the real ICM Instrument status providers.

## Slide 16: New Telemetry System

## Slide 17: Live Status