## Slide 1: ROBOTIC CONTROL SYSTEM
ENVIRONMENTAL REACTIVE SYSTEM

## Slide 2: High level interactions

## Slide 3: Flow of control
Feeds from EMS, TCM, ICM into the ERS are processed and can trigger EnvironmentChangeEvents which are received by the StateModel.
The StateModel maintains a set of condition or state variables to keep track of environment changes - (see OpsUI at the lower left corner) and include:-
  System
  Weather
  Axes
  Intent
  TimeOfDay
  Network
When in the OPERATIONAL state, there is a secondary OperationalStateModel which handles the fine detail of initialization and finalization of observing and switching between modes.
The current state and set of conditions in force determines whether to change state and which ControlAction(s) if any to perform via the OperationsManager.
  E.g. In OPERATIONAL state and Weather is bad -> execute AbortOps action and Close action.
ControlActions are performed by the OperationsManager. They may involve starting transient or mode controller tasks or may involve aborting an operational task.

## Slide 4: State Model

## Slide 5: Operations State Model

## Slide 6: Environmental Reactive System
The ERS is made up from various components:-
  Filters receive input from telemetry feeds from each of the low level systems:-
    EMS (meteo, seeing, cloud, dust)
    TCM (axes, enclosure, mirror-cover, mcp)
    ICM (instruments)
  Criteria are attached to filters – a criterion can only be attached to a single filter but a given filter may feed many criteria.
    Criteria provide simple boolean conditions on the state of the feed:-
      Equals
      Greater
      Less
      One-of
  Rules are attached to criteria
    Indicate a period of time for which the criterion must be satisfied.
    Rules can be combined via AND and OR operations. Potentially others could be added like FUZZY.

## Slide 7: ERS Configuration
The ERS is configured from a file: rules.xml
Structured with sections for:-
  Filters (name, type, feed-ID)
  Criteria (name, filter-ID, condition)
  Rules (name, class, class-config)
  Rules can be nested to any depth as
    Conjuncts (AND)
    Disjuncts (OR)

## Slide 8: Filter config
Filter example:-
    <filter name = "M_HUM_SLOW" class = "AVERAGE">
      <source> METEO </source>
      <category> WMS </category>
      <item> humidity </item>
      <period unit = "mins"> 5 </period>
    </filter>
    Name: M_HUM_SLOW
    Type: Averaging, period 5 mins
    Feed: METEO / WMS / humidity

## Slide 9: Criterion config
Criterion example:-
    <criterion name = "C_WS_HI" class = "GREATER">
      <minimum> 15.0 </minimum>
      <filter> M_WS_FAST </filter>
    </criterion>
    Name: C_WS_HI
    Filter: M_WS_FAST
    Condition: value > 15.0

## Slide 10: Rule config
Rule example:-
    <rule name = "CLOUD_HI" class = "timed">
      <period unit = "mins"> 10 </period>
      <criterion>…….</criterion>
    </rule>
    Name: CLOUD_HI
    Class: timed (condition must be true for specified amount of time)
    Class-config: period = 10 minutes

## Slide 11: Combination rule config
Combination (CONJUNCT) example:- (internal detail hidden)
  <rule name = "ENC_OPEN" class = "CONJUNCT">
    <rule name = "EN1_OPEN" class = "timed"> … </rule>
    <rule name = "EN2_OPEN" class = "timed"> … </rule>
    <rule name = "EN1_IN_POSN" class = "timed"> … </rule>
    <rule name = "EN2_IN_POSN" class = "timed"> …</rule>
  </rule>
  Rule ENC_OPEN is triggered only if ALL the enclosed rules are also triggered, i.e. their enclosed criteria must all satisfied for the required amount(s) of time.

## Slide 12: Flow through ERS layers