## Slide 1: Robotic Control System
Configuration and operation

## Slide 2: Layout of occ filesystem
/occ
  /bin
      various startup and utility scripts
  /common
    /ngat
        NGAT libraries
    /shared
        3rd party libs (jibx, jdom, xerces…)
    /lib
        c libs (libjslalib.so, libngatfits.so…)
  /data
        data generated by various cron scripts
        Eg cloud.dat, dust.dat, ocr.dat…
  /rcs
    /config
        configuration files
    /instruments
        instrument calib data
    /tocs
        ToO accounting
    /scripts
        Various scripts
  /logs
        The rcs logs for the last day
  /tmp
        Temporary logs eg rcs console, various script logs.
  /backup
        Dated backups made using /occ/bin/backup script

## Slide 3: Processes on OCC
RCS
  Started via: /etc/init.d/rcw_init
    This is a watchdog, it restarts the RCS if it falls over or a restart is requested via the OpsUI.
Scheduler
  Started via: /etc/init.d/sched_init
    The deployed version of this script does not have a stop option – there is one in the dev version.
Synoptic Model -Phase2 cache (level 1)
  Started via: /etc/init.d/smp_init
    There is a level 2 cache but this is still experimental it would probably speed up scheduler execution by a factor of around x5 to x10. Again the deployed script has no stop option but the dev version does.
Beam Steering System
  Started via: /etc/init.d/bss_init
    This has to be running as the instruments (O at least) talk to it.

## Slide 4: Main Process
The RCS main launcher is contained in the class
  ngat.rcs.RCS_Controller
It configures and starts all the various subsystems and modules:-
  TCM
    configured via telescope.xml
  ICM
    configured via ireg.xml
  EMS
  ERS
    configured via rules.xml
  TMS
    configured via task.properties
    agent.properties and various mode controllers via
    soca_ops.properties , to_ops.properties, background.properties
  Ops
    configured via tsm_reactive.properties

## Slide 5: RCS Process startup
Initialize logs
Initialize astrometry
Setup CIL service and CIL Proxy
Setup ISS and TOCS
TCM setup
  Configuration
  Start monitoring TCS and AG
ICM setup
  Configuration of Ireg and instrument status providers
  Start monitoring instruments
Legacy providers for LiveData feeds
EMS setup
  Configuration
  Start monitoring WMS, BCS, TNG
ERS setup
  Start processing thread
Monitors setup
  Tracking, Autoguider lock, Instruments, PMC
TMS setup
Ops setup, statemodel and binding to ERS
MCA setup
  Configure BGCA, SOCA, TOCA, CA
A minute or so after everything is setup the time-of-day (PERIOD) and eng/auto (INTENT) state variables, used by the state model are set according to the actual time of day and command line arg (manual or auto).